## Slide 1: Zhang’s Camera Calibration
광학솔루션SW개발팀
조성윤

## Slide 2: 빛의 행동
상(인화지)에서 파이프를 구분 할 수 있을까?
상(인화지)

## Slide 3: Pinhole 카메라
차광막을 설치하고 차광막에 작을 구멍(Pinhole)을 뚫어 놓는다면?

## Slide 4: Pinhole 카메라
Pinhole 크기가 작은 경우
(이상적인 Pinhole 카메라는 Pinhole의 크기가 0 이다.)
Pinhole 크기가 큰 경우
Pinhole 크기가 작을 수록 선명하다. 왜 그러한가?
Pinhole 크기가 작다면 어떤 단점이 있는가?
상이 반전 된다.

## Slide 5: Pinhole Camera Model
Object
Retina Plane
Pinhole
Focal length:
image Plane
Focal length:

## Slide 6: Lens Camera
Pinhole 카메라의 단점을 보완하기 위해 렌즈 카메라를 사용한다.
pinhole 카메라의 Focal length와 렌즈카메라의 Focal length는 같은가?
pinhole 카메라의 Focal length는 Lens Camera의 무엇과 대응되는가?
(1) focal length
(2) Lens position
(3) Lens position - focal length
렌즈 카메라의 단점은 무엇인가?
Chart (Object)
Image Sensor
Pinhole
: Chart(Object) Distance
  : Focal Length
Focusing
Chart (Object)
Image Sensor
Lens
: Chart(Object) Distance
  : Lens Position
  : Focal Length
Focusing
Pinhole 카메라
Lens 카메라

## Slide 7: 3D 좌표계
왼손 좌표계
오른손 좌표계
일반적으로, 둘 중 어느 좌표계를 쓰는가?

## Slide 8: 아핀변환
아핀변환(Affine Transform)
Identity (항등)
Scaling
Reflection (반사)
Shearing (층밀리기)
Rotation (회전)
Translation

## Slide 9: Affine Transform Matrix
(식1)
: 변환 전 2D 좌표
: 변환 후 2D 좌표
: 아핀변환 행렬
은 무엇일까?

## Slide 10: Identity and Scale
Identity (변환 전과 후가 같다)
Scaling
(가로와 세로를 일정 비로 늘리거나 줄인다.)

## Slide 11: Reflection and Shear
Reflection (반사)
(가로축 반사)
(세로축 반사)
(180도 회전)
Shearing (층밀림)
가로축 반전
가 0일 경우 X축으로 만 밀림

## Slide 12: Rotation and Translation
Rotation
Translation
은 Translation을 표현하기 위해 쓰임

## Slide 13: Rotation and Translation
Rotation and Translation
Q: 위의 변환에서, Rotation과 Translation중 어는 것이 먼저 변환되었는가?
는 Scaling, Reflection, Shearing, Rotation 과 관련이 있다.
, 는 Translation과 관련이 있다.

## Slide 14: Pinhole Camera Model (Camera Coordinate)
Pinhole:
Object in Camera Coordinate:
Pinhole
Focal length:
Image(Retina) Plane
Object on Image Plane
Camera Coordinate (Cartesian)

## Slide 15: Pinhole Camera Model (3D Virtual Image Plane)
Pinhole:
Virtual Image Plane(3D)
Pinhole
Focal length:
Focal length:
Object on Virtual Plane(3D):
Image(Retina) Plane
Object on Image Plane
Camera Coordinate (Cartesian)
Object on Virtual image Plane(3D):
Focal length:
or
Object in Camera Coordinate:

## Slide 16: Pinhole Camera Model (2D Virtual Image Plane)
Pinhole:
Virtual Image Plane(2D)
Pinhole
Focal length:
Object on Virtual Plane(2D):
Camera Coordinate (Cartesian)
Focal length:
or
Object on Virtual image Plane(3D):
Object on Virtual image Plane(2D):
Note: and are NOT Equivalent in Homogeneous Coordinate
Object in Camera Coordinate:

## Slide 17: Homogeneous Coordinate
-차원 직교 좌표(Cartesian Coordinate) 를 동차좌표(Homogeneous Coordinate)로 변환하면, 다음과 같이 표현한다.
마찬가지로, 동차좌표(Homogeneous Coordinate)를 직교 좌표(Cartesian Coordinate)로 변환하면 다음과 같이 표현 한다.
만약, 두 개의 Homogeneous Coordinate point , 가 같은 Cartesian Coordinate point로 mapping 된다면, 과 동치(,equivalent)이다. 즉,
따라서, 에 대해서 다음이 성립한다.
Example: 는 과 동치이며, 그것의 직교좌표는 다음과 같다.

## Slide 18: Pinhole Camera Model (Normalized Image Plane)
Pinhole:
Object:
Virtual Image Plane(2D)
Pinhole
Focal length:
Object on Virtual Image Plane(2D):
Camera Coordinate (Cartesian)
Normalized Image Plane(2D)
1
Object on Normalized Image Plane(2D)
:
Object:
Object on Normalized Image Plane(2D): : normalized projection
Object on Virtual Image Plane(2D):
Note:

## Slide 19: Projection Matrix
Projection Matrix(): Project object point to virtual image point .
Using Normalized Coordinate ,

## Slide 20: Image Sensor Coordinate
Pinhole:
Virtual Image Plane(2D)
& Image Sensor Plane(2D)
Pinhole
Focal length:
Object on Virtual Image Plane(2D):
Object on Image Plane(2D):
Camera Coordinate (Cartesian)
Normalized Image Plane(2D)
1
Object on Normalized Image Plane(2D)
:
Image Sensor Plane은 Virtual Image Plane 위에 위치한다.
Image Sensor Coordinate는 로 표현하며, 단위는 Pixel이다.
Object in Camera Coordinate:

## Slide 21: Image Sensor Coordinate
Pinhole:
Virtual Image Plane(2D)
Image Sensor Plane(2D)
Pinhole:
Image Center
Pixel width
Pixel height

## Slide 22: Intrinsic Camera Parameters
In particular, we need to define how the continuous x/y-coordinates() on the normalized image plane map to actual pixel coordinates.
  the (possibly different) sensor scales , in x- and y-direction, respectively,
  the location of the image center = with respect to the image coordinate system (i. e., the optical axis), and
  the skewedness (diagonal distortion) of the image plane (which is usually negligible or zero).
The final sensor coordinates are obtained from the normalized image coordinates as
: Virtual image coordinate
: Normalized image coordinates
Where
: Intrinsic camera parameter Matrix (Affine Projection)
Intrinsic camera parameters:

## Slide 23: World Coordinate
Camera Coordinate (Cartesian)
: World Coordinate (Cartesian)
Corners in Camera Coordinate for each views
view(Image) 1 2 3
Corners in World Coordinate
World Coordinate에서 Corner의 좌표 는 Chart의 위치 또는 자세에 따라(view 1,2,3에 따라) 변하지 않는다.
Camera Coordinate에서 Corner의 좌표 는 Chart의 위치 또는 자세에 따라 (view 1,2,3에 따라) 변한다.

## Slide 24: World Coordinate
Camera Coordinate (Cartesian)
: World Coordinate (Cartesian)
Rigid Transformation: Transform world coordinate to camera coordinate
Pinhole:
Virtual Image Plane(2D)
& Image Sensor Plane
Pinhole
Focal length:
Object on Virtual Image Plane(2D):
Object on Image Plane(2D):
Normalized Image Plane(2D)
1
Object on Normalized
Image Plane(2D):
Object in world coordinate:
Rigid Transformation
Object in Camera Coordinate:

## Slide 25: Rigid (body) Transformation
Let us assume that a rigid 3D object is represented by the point set (: World Coordinate, : image or view index). Under rigid body transformation every (non-homogeneous) 3D point on that object is mapped to a new point(in Camera Coordinate)
is an (orthonormal: ) 3D rotation matrix
is a 3D translation vector
The matrix in (157), which describes arbitrary rotation in 3D, is composed of three individual rotations , , about the , , and axes, respectively:
The complete matrix R for an arbitrary rotation in 3D is obtained as
Note:

## Slide 26: Rigid (body) Transformation
The complete rigid transformation, combining rotation and translation in homogeneous coordinates is then obtained as
: Corner Point Set of th view in Camera Coordinate
: Corner Point Set of th view in World Coordinate

## Slide 27: Extrinsic Camera Parameters
: Image coordinates, :Normalized coordinates
: Camera coordinates
, : World coordinates
: Intrinsic camera parameter Matrix
: Extrinsic camera parameter Matrix: 카메라의 시점에 따라 다름.

## Slide 28: Rodrigues Rotation Formula (Rodrigues vector to Rotation matrix.)
Given a 3D rotation specified by the Rodrigues vector , the corresponding rotation matrix can be found as follows. First, we extract the rotation angle (with ) and the unit direction vector by
and ,

## Slide 29: Rodrigues Rotation Formula (Rodrigues vector to Rotation matrix.)
The associated rotation matrix is defined as
where is the 3x3 identity matrix, and
is the cross-product matrix ()
Rodrigues’s formula in matrix form and matrix expansion.

## Slide 30: Rodrigues Rotation Formula (Rotation matrix to Rodrigues vector)
Rodrigues’s formula in matrix form and matrix expansion.
Given rotation , We find Normalized Rodrigues vector .
Also, Given rotation , We find Normalized Rodrigues vector angle .
=
, ()
Finally, Given rotation , We find Normalized Rodrigues vector .
, we need exception case for

## Slide 31: Pinhole Camera Parameters
: Intrinsic camera parameter Matrix, Intrinsic camera parameters: ()
: Extrinsic camera parameter Matrix (), Extrinsic camera parameters: ()
Pinhole:
Virtual Image Plane(2D)
& Image Sensor Plane
Pinhole
Focal length:
Object on Virtual Image Plane(2D):
Object on Image Plane(2D):
Normalized Image Plane(2D)
1
Object on Normalized
Image Plane(2D):
Object in world coordinate:
Rigid Transformation
Object in Camera Coordinate:

## Slide 32: Lens Distortion
Decentering errors: caused by a displacement of the lens center from the optical axis (this is mostly taken care of by the variable offset .
Radial distortion caused by variations in light refractions, which is typically apparent in wide-angle lenses (“barrel distortion”).
we define a general distortion function warp: , which maps an undistorted 2D coordinate x to a distorted 2D coordinate undistorted 2D coordinate to a distorted 2D coordinate (again in the normalized projection plane) by
where is a vector of distortion parameters.
With this definition, we can reformulate the projection process
: 2x1 Point(Object) on Distorted Normalized plane(2D)
: 2x1 Point(Object) on Normalized plane(2D)
: Intrinsic Matrix
: Pont(Object) in World Coordinate
: Extrinsic Matrix

## Slide 33: Lens Distortion (Radial distortion model)
Pinhole:
Normalized Plane(2D)

## Slide 34: Lens Distortion (Radial distortion model)
In the normalized projection plane, the optical axis intersects the image plane at , which is assumed to be the center of the lens distortion. The radial distance of a projected point from the center can thus be simply calculated as
The distortion is assumed to be radially symmetric, i. e., it only depends on the original radius of a given point , as defined in the equation. The distortion model can thus be specified by a single-variable function such that the distorted radius is
Consequently , the warped projection point is ˜xi = warp(xi, k), with
The function specifies the (positive or negative) radial deviation for a given radius . A simple but effective radial distortion model is based on the polynomial function
with the (unknown) coefficients

## Slide 35: Summary of the projection process
World-to-camera transformation: Given a point (X, Y,Z)⊺, expressed in 3D world coordinates, its position in the 3D camera coordinate system is specified by the viewing transformation
Projection onto the “normalized” (ideal) image plane: The perspective projection from the 3D-point (in 3D camera coordinates) onto continuous, normalized 2D coordinates on the image plane is defined.
Radial lens distortion: The normalized 2D projection coordinates are subjected to a non-linear radial distortion with respect to the optical center , expressed by the mapping
Affine 2D transformation to sensor coordinates: The normalized projection points are finally mapped to the scaled and skewed sensor coordinates (see Eqn. (13)) by the affine transformation
: : Projection function with parameter

## Slide 36: Camera Calibration
Intrinsic Parameters (5 parameters)
  : (: focal length, : sensor scales x-direction)
  : (: focal length, : sensor scales y-direction)
  : (: focal length, :skewness)
  , : optical center in image coordinate
Extrinsic Parameters (6 parameters)
  : translastion
  (3x3) or , Rodrigues form: rotation
Radial Distortion Parameters (2 parameters
  :

## Slide 37: Homography
Homography: 한 평면을 다른 평면에 투영(Projection) 시켰을 때 투영된 대응점들 사이에서는 일정한 변환 관계가 성립한다. 이 변환 관계를 Homography라고 한다.

## Slide 38: Plane-based “self” calibration
The popular camera calibration method by Zhang uses a few (at least two) views of a planar calibration pattern, called “model” or “target”, whose layout and metric dimensions are precisely known. The calibration procedure works roughly as follows:
Images , . . . , ,. . ., of the model are taken under different views by either moving the model or the camera (or both).
From each image (), sensor(Corner) points , …,…,are extracted (observed in sensor coordinate), assumed to be in 1:1 correspondence with the points(,…, ,…, ) on the model plane(in world coordinate).
Model in world coordinate
images

## Slide 39: Plane-based “self” calibration
From the observed points, the associated homographies (: view index, ) (linear mappings from the model points and the observed 2D image points) are estimated for each view . (: point index)
From the view homography set , the five intrinsic parameters () of the camera are estimated using a closed-form (linear) solution, ignoring any lens distortion at this point. views give a unique solution (up to an undetermined scale factor ). If the sensor plane is assumed to be without skew (i. e., , which is a reasonable assumption) then images are sufficient. More views generally lead to more accurate result.
Once the camera intrinsic parameters are known, the extrinsic 3D parameters , are calculated for each camera view 𝒊
The radial distortion parameters 𝒌 are estimated by linear least-square minimization
Finally, using the estimated parameter values as an initial guess ((, (,,(or ):step 3~6), a all parameters are refined by non-linear optimization over all M views

## Slide 40: Plane-based “self” calibration
From the observed points, the associated homographies (: view index, ) (linear mappings from the model points and the observed 2D image points) are estimated for each view . (: point index)
- How to find for given and ?: SVD and non-linear optimization.
From the view homography set , the five intrinsic parameters () of the camera are estimated using a closed-form (linear) solution, ignoring any lens distortion at this point. views give a unique solution (up to an undetermined scale factor ). If the sensor plane is assumed to be without skew (i. e., , which is a reasonable assumption) then images are sufficient. More views generally lead to more accurate result.
Once the camera intrinsic parameters are known, the extrinsic 3D parameters , are calculated for each camera view 𝒊. –We need exact rotation matrix : using SVD, we can obtain exact rotation
The radial distortion parameters 𝒌 are estimated by linear least-square minimization(Pseud inverse).
Finally, using the estimated parameter values as an initial guess ((, (,,(or : Rodrigues Rotation Formula):step 3~6), a all parameters are refined by non-linear optimization(LM (Levenberg–Marquardt ) Method) over all M views

## Slide 41: Optimization Method
: estimated image coordinates of th point in th view
, th view camera parameters.
: Camera parameter set
It implies . : measured image coordinates of th point in th view
, .
sum of square error
We find optimized camera parameter set that minimizes sum of square .
is nonlinear function of . So, we need initial camera parameter to solve nonlinear solution problem. : it is obtained by step3~6
LM(Levenberg–Marquardt ) Method is proper to solve the problem.

## Slide 42: Mathematic Tools
Linear Solution Problem
Pseudo inverse
- SVD(singular value decomposition)
Non linear Solution Problem
Newton Method
LM Method
Geometric Transform
Affine Transform
Homography
Rodrigues Rotation Formula

## Slide 43: Reference
Z. Zhang, A Flexible New Technique for Camera Calibration, ‎2000.
W. Burger, Zhang’s Camera Calibration Algorithm: In-Depth Tutorial and Implementation, 2016