## Slide 1
- 공유 내용
타당성 검토 과제 calibration concept
Geometrical calibration 코드 분석 내용(GMAPD 이미지 생성 포함)
Range calibration 코드 분석 내용
Calibration Data Input / Output

## Slide 2
 | XY(Geometric) Calibration | Z(Range) Calibration
Space | 3m x 2m | 5m x 2m
실험 방법 |  | 
타당성 검토 concept
3m
SWIR LEDs
LiDAR
XY Cal.용 Target
Mirror
Diffuser
5m
2m
2m
3) 기술 검증
5m x 4개 Mirror = 20m 구현
4 / 8

## Slide 3
Generating GMAPD Image Diagram
Generate_gmapd_images.py
Initialize config parameters
Function
Read log data
Data
Log config file path
Process config file path
Intensity map
Corresponding azimuth angles
Generate Intensity map
Number of sweeps
Azimuth bounds degree
Bin bounds(0~4000)
Sort azimuth angles
& Stack data
Azimuth angle range
Column side
(left or right)
*Library

## Slide 4
Geometric Calibration Diagram
Calculate_geometric_cal.py
Run_geometric_calibration
Function
run_gonio
_tracker
Preprocess
Image
(interpolate2D
&Median blur)
run_rot
_tracker
run_template
_match
Data
Fiducial info
Config file path
Range offset
Azimuth degree
Elevation degree
Azimuth Skew
Elevation fov
Rotation stage position degree
Fiducial information
Configuration data
run_template
_match
Preprocess
Image
(interpolate2D
&Median blur)

## Slide 5
Range bias Calibration Diagram
Intrinsic_cal_template.py
Generate_ground_truth
Function
Data
GT data(Riegle)
Range bias
GT transformation data
Run_log_analyzer
Run_target_analyzer
Statistical information
(ex. Range tolerance, confidence min…)
Extract_scalars&statistics_
from_PC&GT
Argo point cloud data
Log data file path
Loaded log data
Stdev
Mean
Percentile (input&GT both)
Get_mean_
range_bias

## Slide 6
Geometric Calibration Diagram
Calculate_geometric_cal.py
run_
geometric_
calibration()
Function
Data
Log data
fiducials: indicies referring to keys of fiducials to use to calculate geometric calibration
logging_config_path: path to logging configuration yaml
process_config_path: path to intrinsic calibraton processing config yaml
logfolder_path: Path to directory containing logs and gmapd swath images
override_lidar_name: Optional string to substitute lidar name in logging config
override_mr_rangeoffset_path: Optional Path to substitue mr range offset file
override_lr_rangeoffset_path: Optional Path to substitue lr range offset file
override_calibration_output_path: Optional Path to outputs folder to write calibrations
azim_offset_deg: fixed degree offset in azimuth added to bounding boxes for MRLR lidar comparison
elev_offset_deg: fixed degree offset in elevation added to bounding boxes for MRLR lidar comparison
zero_range_offset: if True, calculate only geometric corrections and set range offsets to zero
no_offset_adjust: if True, create only backtest file
One_
fid_
calc()
fiducial: key value for fiducial to analyze from process_config
logging_config: dict with logging config values e.g. load_intrinsic_test_config(os.fspath(logging_config_path), globs=globals())
process_config: dict with ical process config values e.g. load_intrinsic_test_config(os.fspath(ical_config_path), globs=globals())
logfolder_path: Path to directory containing logs and gmapd swath images
Run_
gonio_
tracker()
transceiver: Transceiver('MR') or Transceiver('LR')
fid_ind: which fiducial key from configs to use
logging_config: dict with logging config values e.g. load_intrinsic_test_config(os.fspath(logging_config_path), globs=globals())
process_config: dict with ical process config values e.g. load_intrinsic_test_config(os.fspath(ical_config_path), globs=globals())
logfolder_path: Path to folder containing gmapd swath images
manual_offset_px: offset of center of template in +x (right), +y (down)
adjust_offset: flag to allow readjustment of template center
valid_stdevs: float for how many standard deviations from others a template match can be to be used
gonio_folder: Path to folder containing numpy array of gmapd swath images from gonio scan
Initialize_
Fiducial_
Tracker
Find_
template()
serial_number: serial number of the lidar
stage_type: type of stage, e.g. 'rot', 'gonio'
transceiver_type: type of transceiver, e.g. 'MR', 'LR'
range_offset_m: offset of the range.
validated array of filenames
validated position
fiducial_min_size_m: minimum size of the fiducial
range_guess_m: guess for the range
gonio_zoffset_m: z-offset for the gonio
gonio_pointing_deg: pointing angle for gonio
s
use_resampled: sets option to use a resampled image
match_method: index for the match method from opencv, e.g. cv2.TM_CCOEFF.
ref_image_ind: index of the reference image
array_column: column index of the FPA: 0 or 1
template
Ref_image_ind = 10
Filearray+”.npy”
Azimuth_angles of imagedata = ref[2]
Run_
template_
match()
Target azimuth angles (fiducial center pixel to angle)
Target elevation angles (fiducial center pixel to angle)
Azimuth positions of the lidar
template: template to match
folder: folder to load output arrays from
filearrays: array of filenames of output arrays to load
positions_deg: positions of the stage
 positions = zip(*sorted_positions)
 sorted_positions = sorted(positions_dict.items(), key=lambda x: x[1])
array_column: the FPA column number (0 or 1)  [0, 1]
match_method: the match method, indicated with a number from cv2 (opencv)
use_resampled: option to resample angles, using resampled_spacing_deg
elevation_angles_deg: the elevation angles
resampled_spacing_deg: the spacing when resampling. See option 'use_resampled'
blur: factor for blurring
show_positions: option to show position in the plot
show_zoom: option to show zoom in the plot
show_correlations: option to show correlations in the plot
Calc_
fit()
Fid_azim  center fiducial angle
Fid_elevs  center fiducial angle
positions_deg(gonio_tilt_deg): positions of the stage  positions = zip(*sorted_positions)
 sorted_positions = sorted(positions_dict.items(), key=lambda x: x[1])
fit_range  validate template match score for individual scan data
skew line fit: numpy array of polynomial fit coefficients of the skew line
fov line fit: numpy array of polynomial fit coefficients of the field-of-view line
Calc_
expected_ target_
elevation()
target_r_m: r-coordinate of the target  Range_guess = 21.7(meters)
target_z_m: z-coordinate of the target = 0
zoffset_m: z-offset in meters = 0.10505
gonio_tilt_deg: gonio tilt in degrees = 0
Polyfit()
Target_elevation_expected
Target_elevation_angles_deg
Positions_deg
Target_azimuth_angles_deg
Expected target elevation angles
Skew_line_fit
Fov_line_fit
Run_
rot_
tracker()
Sine_azim_fit.x
transceiver: Transceiver('MR') or Transceiver('LR')
fid_ind: which fiducial key from configs to use
logging_config: dict with logging config values e.g. load_intrinsic_test_config(os.fspath(logging_config_path), globs=globals())
process_config: dict with ical process config values e.g. load_intrinsic_test_config(os.fspath(ical_config_path), globs=globals())
logfolder_path: Path to folder containing gmapd swath images
manual_offset_px: offset of center of template in +x (right), +y (down)
adjust_offset: flag to allow readjustment of template center
valid_stdevs: float for how many standard deviations from others a template match can be to be used
gonio_folder: Path to folder containing numpy array of gmapd swath images from gonio scan
Azimuth_offset_rad
Elevation_rad

## Slide 7
Geometric Calibration Data Input/Output
Center X,Y difference
coordinate in pixels
Skew fit
FOV fit
Azimuth offset
Calc_fit
Match_template
GT image, angle data
Input image data
Number rounding
elevation_rad
Azimuthh_offset_rad
Function
Data
.yaml file
.npy file
Capture
GMAPD 변환
Range data 변환
Geometric Parameters 생성
Ranging Parameters 생성
Depth Map
Intensity Map