## Slide 1: S-LiDAR Cal. (Dark, TDC, P2P)
Item | 인원 | 6월2주 | 6월3주 | 6월4주 | 7월1주 | 7월2주 | 7월3주 | 7월4주 | 8월1주 | 8월2주 | 8월3주 | 8월4주 | 11월
Dark, TDC, P2P Cal. 장비 | 성동현 이동건 이석민 |  |  |  |  |  |  |  |  |  |  |  | 
DNL용
IR 광원
발주
P2P
광원설계
EVK
입고
P2P
장비
발주
Dark
Cal
검증
TDC
Cal
검증
w/ IR광원
실거리
TOF
Chart
측정
P2P
입고
검증
통합
Cal
장비개발
의사결정
통합
Cal
장비
설계
통합
Cal
장비
발주
입고
ACE d-TOF Sensor Calibration 방식을 자사 S-LiDAR 에 적용
전반적이 Calibration 의 방식은 동일하지만 자사 S-LiDAR 에 적합한 장비 구성으로 Modification

## Slide 2: Lens Calibration
Geo Cal.
Depth Cal.
FPN Cal.
TDC Cal.
measure
Spot finding
Dark Box
LPFF
Rail
P2P
Jasper Calibration BM process
LPFF TDC Linearization
Python code for TDC linearization
00
01
10
11
V (LSB)
Definition of Differential Non-Linearity
00
01
10
11
V (LSB)
Ideal TDC
Conventional TDC
Jasper의 DNL 측정값 DNL [0.71, 1.66] 일 때 양품 판정. 통상적으로 [0.8, 1.2] in Jasper case

## Slide 3: Lens Calibration
Summarized Lens Calibration process
Print a pattern and attach it to a planar surface.
Take several images with different locations and orientations by moving either the plane or camera.
Detect the corners of the chessboard.
Estimate intrinsic and extrinsic parameters.
Refine the found parameters.
Obtain the distortion parameters and undistort the image.
Repeat 4~6 until all the parameters converge.
Corner detector algorithm.
Zhang’s technique.
The Levenberg-Marquardt algorithm.
The Brown-Conrady model.

## Slide 4
Lens Calibration
고객가치
새로운 시도
집요한 실행

## Slide 5: Lens Calibration: Classification
Errors in Geometrical optics
Monochromatic aberrations
Aberrations
Chromatic aberrations
Spherical aberrations
Coma
Astigmatism
Field curvature
Distortions
Radial
Tangential
Barrel
Pincushion
Mustache
etc…
The principal plane is a ‘plane’ only in the paraxial region.
Caused by the Paraxial approximation. → The first-order theory,
The incident cone of rays strikes the lens asymmetrically.
The actual index of a material is a function of frequency.
Ludwig Von Siedel first studied these aberrations in 1850s.
It is often called Siedel aberrations.
Marginal rays are bent too much or less.
Planar object normal to the optical axis is imaged as a plane only in the paraxial region.
Different areas of the lens has different focal lengths and different magnifications.
Can be modeled with Brown-Conrady model
A fee library is provided by OpenCV

## Slide 6: Lens Calibration: Blur-related aberrations
Spherical aberration
Coma (Comatic aberration)
Astigmatism
Field curvature
Optical axis

## Slide 7: Lens Calibration: radial distortions
The three most common radial distortions
Pincushion distortion
(negative radial distortion)
Barrel distortion
(positive radial distortion)
Mustache distortion
(complex distortion)
degree 2
degree 4
degree 2

## Slide 8: Lens Calibration: pin hole camera model
The pinhole camera model
Fig 1. Pinhole camera model.
Fig 2. Image plane of the pinhole camera model.

## Slide 9: Lens Calibration: pinhole camera model
Camera matrix (Projection matrix)
optical axis
: focal length in pixel unit.
: skew coefficient. Usually 0 for modern camera
: the coordinate of the principal point in pixel unit.
Skew coefficient.
The world coordinate and the image coordinate.
Image plane and

## Slide 10: Lens Calibration
The homography matrix
A planar surface and the image plane
Rotated and translated camera position
The planar homography maps the transformation between two planes.
It is a matrix but with 8 DOF. It is normalized with or .
can be obtained by using the pseudo-inverse method.
The camera matrix is one kind of homography matrix.

## Slide 11: Lens Calibration
Zhengyou Zhang’s Camera Calibration method
A point in the image plane:
A point in the world plane:
: intrinsic parameters (focal length, principal point)
: Rotation matrix
: Translation matrix
: Scale factor

## Slide 12: Lens Calibration
Zhengyou Zhang’s Camera Calibration method
We now have the homography matrix ,
We assume the model plane is on . Then,
where is an arbitrary scalar and .
If we dot product both side with , we have
Using the knowledge that and are orthonormal, we have

## Slide 13: Lens Calibration
Zhengyou Zhang’s Camera Calibration method
We can get two constraints from the above equation.
Let . Then is symmetric.
Define a six-dimensional vector and such that
Then we can readily derive that
where is the th column of .
Inserting the above into the two constraints, they can be rewritten as,
Let’s denote .

## Slide 14: Lens Calibration
Zhengyou Zhang’s Camera Calibration method
If there are images, by stacking such equations, we have
where is a matrix.
When , is obtained and then is known.
All the intrinsic parameters are obtained.
Solution: eigenvectors of with the smallest eigenvalues.
where is not exist.
Once the intrinsic parameters are obtained, the extrinsic parameters for each image are readily computed.
Since ,

## Slide 15: Lens Calibration
OpenCV python test code: Spot searching
Before
After

## Slide 16: Lens Calibration
Before
After
OpenCV python test code: Undistort the image
Barrel distortion

## Slide 17: Lens Calibration
Algorithm required for Lens calibration
Zhengyou Zhang’s technique. Required to calibrate the lens and undistort the image. To obtain the intrinsic/extrinsic parameters.
The Levenberg-Marquardt Algorithm Required for obtaining the homography matrix estimation. Required for minor correction of the coordinate of the points on the image plane.
Corner detection algorithms. Required for accurate detection and localization of checkerboard corners.

## Slide 18: Lens Calibration
90cm
80cm
100cm
Lens Calibration in Jasper

## Slide 19: Lens Calibration
Can it be directly applied to IMX459?
LiDAR has all three coordinates, . Then why should we adopt the calibration method for the 2D camera? Shouldn’t we calibrate LiDAR using the spherical coordinate?