## Slide 1: Mobis Lens Cal
cm
cm
LED dot 사이 간격
1150 mm
550 mm
가로 24개, 세로 12개, 총 288개
모비스의 설명 내용
IR 광원 + 메탈차트
차트 거리 : 0.5~5m, 균일도 90%, 288 Point,
차트 Size : 1.4 m x 0.8 m
광원 파장: 940 nm
차트는 고정이고, 6축 Stage 이동하여 카메라를 회전하여 5회 촬영 예정.
영역은 중심*1 / 상하 외곽*4 을 고려 중입니다.
해상력의 기준인 SPAD Pixel size로 10um 기준.
균일도 90%라는 말은 이해 불가. LED power 가 균일하다는 뜻인지, 간격이 일정하다는 뜻인지. 일정하다면 28.8개는 5cm가 아니라는 뜻인지. 모든 간격이 4.75cm 혹은 5.25cm 라는 뜻인지.
고려 중인 것으로 보아 실험은 아직 진행 안한듯.
SPAD sensor가 가로세로 10um. (Sony IMX459 센서 pixel 크기)
심도 내에 chart가 위치했을때 5 mm 이상이면 LED dot을 구분 가능. 따라서 5cm 는 충분한 간격임.

## Slide 2: Mobis Lens Cal
분석 결과
모든 사진에서 공통적으로 관측된 점만을 사용해야 하므로, mobis의 XY Cal concept은 중앙 부분의 LED dot만 써야함. 따라서 모든 영역을 맵핑하는 것은 아무런 쓸모 없는 일.
‘외부 변수 최소화’, ‘차트 대비 넓은 영역’, ‘다양한 카메라 모듈 대응 가능 구조’는 너무나 당연한 말. catch phrase 를 위해 의미 없는 말을 덧붙인 것.
단점 정리:
외각의 LED dot 은 쓸 수 없으므로 왜곡 보정이 잘 안 될 것.
사진 보다 chart가 큼. 따라서 각 사진에 관측된 LED dot 이 서로 같은 LED dot 인지 확인하는 작업이 필수로 진행되어야 함. 이는 매우 번거롭고 소모적인 작업임.
288 개의 LED 중 중앙의 일부만 쓸 수 밖에 없으므로 돈 낭비, 공간 낭비
모비스의 설명 내용
차트의 각 부분을 촬영하고 조합하여 이미지 상 모든 영역을 맵핑함
외부변수 영향을 최소화 하여 데이터화 함.
차트 대비 넓은 영역의 이미지 데이터 확보가능.
다면 차트 대체 효과 및 다양한 카메라 모듈 대응 가능한 구조
왜곡 계산 가능한 영역

## Slide 3: Mobis Lens Cal
분석 결과
축 translation 3개 축 및 rotation 3축. 총 6축
Translation 축: 5mm 이상이면 구분 가능하므로, 0.001 mm 단위의 해상도는 충분.
Rotation 축: 마찬가지로 해상도는 충분. Dynamic range는 . 우리의 concept 은 이상이면 되므로, S-LiDAR에 적용 가능.

## Slide 4: Mobis Lens Cal
모비스의 설명 내용
6축 Stage + 메탈 차트 + 940nm 광원을 배치를 통해 Intrinsic calibration
6축 stage는 라이다의 FOV를 커버할 정도의 이동량과 SPAD Pixel 단위에대한 해상력만 가질 정도의 사양이면 충분 할 것으로 예상
라이다 광원만으로는 측정할 Intensity가 부족할 수 있기에 메탈차트와 940nm의 조명을 배치하여 calibraion을 진행하는 것이 유리할 것으로 예상됩니다.
분석 결과
Chart 가 0.5m ~ 50m 까지 움직이는 것으로 보아 XY Cal 과 Z Cal 을 하나의 board 를 사용하여 동시에 진행하는 것으로 추정됨.
LED 앞에 십자가 형태의 구멍이 뚫린 형태는 아닌 것으로 추정됨.
메탈 차트가 intensity 보강에 어떤 효과가 있는 것인지는 이해가 필요함.

## Slide 5: Mobis Lens Cal
Zhang’s technique + fisheye distortion model 로 보아 OpenCV 사용하는 것으로 추정됨.
Tangential distortion 이 설명에는 적혀 있으나, 메일로는 계산하지 않는 것을 확인.
Radial distortion 만 계산.

## Slide 6: Chart concept
암막 커튼 (암막 블라인드)
2. Depth cal. mode: linear stage를 통한 평행이동
(Mirror를 활용한 Depth cal. Process 시작)
1. Geo cal. mode: linear and rotation stage 활용 (LED chart와 stage를 활용한 이미지 획득)
LED Chart
Linear stage for x-dir
Linear stage for y-dir
Rotation stage for z-dir
(Yaw)
Rotation stage for y-dir (Pitch)
Module and stage
Rx
Tx
chart 교체

## Slide 7: Chart concept
차트 정면
차트 윗면
차트 옆면
cm
S-LiDAR
1 m
cm
cm
cm
LED dot 사이 간격
1 m
20 cm
Chart #1
Chart #2
차트 윗면
cm
S-LiDAR
차트 정면
1 m
20 cm

## Slide 8: Fiberoptics
Fiber categories based on propagation:
  Single Mode Fiber (SMF)
  Multimode Fiber (MMF)
Categories based on refractive index profile
  Step Index Fiber (SIF)
  Graded Index Fiber (GIF)
Function as a light guide

## Slide 9: Fiberoptics
Dispersion
Modal dispersion
Chromatic dispersion
Polarization mode dispersion
Input signal spreads out as it propagates along the fiber.
Significant in multi-mode fibers
Occurs by the different speeds of light rays.
Different speeds due to the dispersive property of the material.
Different speeds in the core and the cladding.
Material dispersion:
Waveguide dispersion:
Different speeds for different polarization axis.

## Slide 10: Fiberoptics: Chromatic dispersion
Images from: https://community.fs.com/blog/types-of-optical-fiber-dispersion-and-compensation-strategies.html
Material dispersion
Waveguide dispersion
Particularly significant in single mode optical fiber.

## Slide 11: Fiberoptics: Polarization mode dispersion
Images from: https://community.fs.com/blog/types-of-optical-fiber-dispersion-and-compensation-strategies.html
Polarization mode Dispersion
PMD is affected by fiber manufacturing, cabling, installation, and operating conditions.
For normal fiber, the speed of each polarization is different, because of non-concentricity or ovality.

## Slide 12: Fiberoptics: Modal dispersion
A planar waveguide (easy to understand).

## Slide 13: Fiberoptics: Modal dispersion
TE mode propagation in a planar waveguide.
The phase difference between points A and C.
Only certain and can satisfy this condition for a given integer .
: Propagating along the -axis.
: Propagating with an oblique angle.

## Slide 14: Fiberoptics: Modal dispersion
The schematic of the step-index optical fiber.
Cylindrical Coordinate
The step-index fiber
EM wave in an optical fiber should be described by solving Maxwell’s equations.
Maxwell’s equations in free space
To accurately determine the distance to the target when the light passes through the optical fiber,
the electromagnetic fields inside of the optical fiber should be accurately described.
For this sake, we will solve Maxwell’s equations in optical fiber using cylindrical coordinates.

## Slide 15: Fiberoptics: Modal dispersion
Maxwell’s equations in free space
① If the medium is linear,
② and if the medium is non-dispersive,
③ and if the medium is isotropic,
④ and if the medium is homogeneous,
in other words,
⑤ and if the medium is non-magnetic,

## Slide 16: Fiberoptics: Modal dispersion
Maxwell’s equations in free space
Applying curl on both sides of the Faraday’s law,
from the vector identity,
Substitute where is the speed of light to find the wave equation
In cylindrical coordinates, a vector can be written as,
and the curl equations are defined as,
Then the vector Laplacian, the left-hand side of the wave equation, is equal to

## Slide 17: Fiberoptics: Modal dispersion
The wave equation in cylindrical coordinate is then,
can be directly derived from the last equation.
To use the separation of variables, we assume the factored form for ,
Substituting this into the above equation, we have

## Slide 18: Fiberoptics: Modal dispersion
We have
where is an arbitrary constant. From the last equality, we have
Now divide by , we have
where .

## Slide 19: Fiberoptics: Modal dispersion
To obtain the solution of the Helmholtz equation in cylindrical coordinates, we again assume that
The first equality is called the Helmholtz equation.
Substituting this into the above equation and dividing by yields,
where is constant. From the last equality we have

## Slide 20: Fiberoptics: Modal dispersion
Now the first equality becomes
Letting and multiplying to both sides, we have
In a manner analogous to the previous procedure,
Also, we have the equation,
It is called Bessel’s differential equation.

## Slide 21: Metalens: Diffraction in lens
Airy disk

## Slide 22: Chart concept
구 분 | Spec
X-dir. linear stage | Distance: 0.5m ~ 1.0m
Y-dir. linear stage | Distance: 1.0m~2.0m
Rotation stage (y, z-dir.) | Resolution: 0.1 Degree
XY linear stage
2 Axes Motorized goniometer

## Slide 23: Chart concept
module
m
module
m
chart의 크기를 약간 축소. (가로 1.4m 1m, 세로 25cm 20cm) 약간의 tilt와 평행이동을 하더라도 chart의 모든 LED가 항상 detect 되어야 S/W개발에 용이. 회전 모터는 최소 상하 , 좌우 의 range에서 단위의 분해능이 필요할 것.
축 회전
축 회전
module
module
cm

## Slide 24: Chart concept
LED chart
Module
Rotation stage
One-chart moving concept schematic
Linear stage
1 m
차트 정면
S-LiDAR
차트 윗면
차트 옆면
cm
cm
1 m
cm
cm
LED dot 사이 간격