## Slide 1
Lens Calibration
고객가치
새로운 시도
집요한 실행

## Slide 2: Lens Calibration
Jasper
Errors in Geometrical optics
Monochromatic aberrations
Aberrations
Chromatic aberrations
Spherical aberrations
Coma
Astigmatism
Field curvature
Distortions
Radial
Tangential
Barrel
Pincushion
Mustache
etc…
The principal plane is a ‘plane’ only in the paraxial region.
Caused by the Paraxial approximation. → The first-order theory,
The incident cone of rays strikes the lens asymmetrically.
The actual index of a material is a function of frequency.
Ludwig Von Siedel first studied these aberrations in 1850s.
It is often called Siedel aberrations.
Marginal rays are bent too much or less.
Planar object normal to the optical axis is imaged as a plane only in the paraxial region.
Different areas of the lens has different focal lengths and different magnifications.

## Slide 3: Lens Calibration
Jasper
Errors in Geometrical optics
Monochromatic aberrations
Aberrations
Chromatic aberrations
Caused by the Paraxial approximation. → The first-order theory,
Spherical aberrations
Coma
Astigmatism
Field curvature
Distortions
Radial
Tangential
Barrel
Pincushion
Mustache
etc…
Can be modeled with Brown-Conrady model
A fee library is provided by OpenCV

## Slide 4: Lens Calibration
Jasper
Spherical aberration
Coma (Comatic aberration)
Astigmatism
Field curvature

## Slide 5: Lens Calibration
Jasper
The three most common radial distortions
Pincushion distortion
(negative radial distortion)
Barrel distortion
(positive radial distortion)
Mustache distortion
(complex distortion)
degree 2
degree 4
degree 2

## Slide 6: Lens Calibration
Jasper
OpenCV python test code: Spot searching
Before
After

## Slide 7: Lens Calibration
Jasper
Before
After
OpenCV python test code: Undistort the image
Barrel distortion

## Slide 8: Lens Calibration
Jasper
Can it be directly applied to IMX459?

## Slide 9: Lens Calibration
Jasper
LiDAR has all three coordinates, . Then why should we adopt the calibration method for the 2D camera? Shouldn’t we calibrate LiDAR using the spherical coordinate?

## Slide 10
Error Source in dToF LiDAR with SPAD sensor
고객가치
새로운 시도
집요한 실행

## Slide 11: Error Source in dToF LiDAR with SPAD sensor
SPAD
Current-Voltage Characteristics (I-V)
Dark Count Rate (DCR)
Fill Factor (FF)
Photon Detection Probability (PDP)
Timing Jitter
After-pulse Probability
TDC
DNL
Clock speed
Lens

## Slide 12: Error Source in dToF LiDAR with SPAD sensor
Examples of Geiger-Mode Operation

## Slide 13: Error Source in dToF LiDAR with SPAD sensor
Examples of Geiger-Mode Operation
Since SPAD can detect a single photon,
there is no need for setting threshold voltage.
Image from

## Slide 14: Error Source in dToF LiDAR with SPAD sensor
Examples of Geiger-Mode Operation
Since SPAD can detect a single photon,
there is no need for setting threshold voltage.