## Slide 1: XY Calibration LED Chart

## Slide 2: ▣ System Overview(XY Cal)
System Dimension [W x D x H] : 1,100x 1,100 x 1981 mm
The current design may differ from the actual product.

## Slide 3: ▣ System Overview(Frame, Unit)
전면 DOOR
하부 DOOR
배기 FAN
좌우 동일
급기 FAN
좌우 동일
The current design may differ from the actual product.
LED Chart
Stage

## Slide 4: ▣ System Overview(Stage)
Y축.
ST : ±200mm
X축.
ST : ±200mm
Z축.
ST : ±200mm
Tx축.
θ: ±20°
Ty축.
θ: ±20°
R축.
θ: ±30°
The current design may differ from the actual product.
# X-Y-Z Spec.
X축 : ±200mm 0.1mm Step
Y축 : ±200mm 0.1mm Step
Z축 : ±200mm 0.1mm Step
# Tx-Ty-θ Spec.
Tx축 : θ: ±20° 0.01 ° Step
Ty축 : θ: ±20° 0.01 ° Step
θ 축 : θ: ±30° 0.01 ° Step

## Slide 5: ▣ System Overview(Chart)
The current design may differ from the actual product.
LED MCPCB
LED MCPCB
40X10=400EA 적용.
25mm 간격 배열.
245
995

## Slide 6: ▣ System Overview(이동형 Chart)
System Dimension [W x D x H] : 820x 600 x 1340.9 mm
The current design may differ from the actual product.

## Slide 7: ▣ System Overview(이동형 Chart Frame)
The current design may differ from the actual product.
LED MCPCB
이동식 LED 스위치 박스.
전장 및 LED 컨트롤박스.
이동형 바퀴 및 스톱퍼
일체형.
발광 방향.

## Slide 8: ▣ System Overview(이동형 Chart)
The current design may differ from the actual product.
LED MCPCB
13X11=143EA 적용.
50mm 간격 배열.
820
600

## Slide 9: ▣ System Overview(이동형 Chart, XY LED Chart)
The current design may differ from the actual product.
현재의 컨셉은 LED배열 발광 (25mm, 50mm, 100mm)을 기준으로 제작되었습니다. 개별 발광 컨셉으로 제작될 경우, 컨셉이 변경될 수 있습니다.

## Slide 10
THANK YOU
for your attention!