## Slide 1: The Optical Fiber and Light Wave Propagation
Xavier Fernando
Ryerson Comm. Lab

## Slide 2: The Optical Fiber
Fiber optic cable functions as a ”light guide,” guiding the light from one end to the other end.
Fiber categories based on propagation:
  Single Mode Fiber (SMF)
  Multimode Fiber (MMF)
Categories based on refractive index profile
  Step Index Fiber (SIF)
  Graded Index Fiber (GIF)

## Slide 3: Step Index Fiber
Uniform ref. index of n1 (1.44 < n1 < 1.46) within the core and a lower ref. index n2 in the cladding.
The core and cladding radii are a and b. Typically 2a/2b are 8/125, 50/125, 62.5/125, 85/125, or 100/140 µm.
SIF is generally made by doping high-purity fused silica glass (SiO2) with different concentrations of materials like titanium, germanium, or boron.
n1
n2
n1>n2

## Slide 4: Different Light Wave Theories
Different theories explain light behaviour
We will first use ray theory to understand light propagation in multimode fibres
Then use electromagnetic wave theory to understand propagation in single mode fibres
Quantum theory is useful to learn photo detection and emission phenomena

## Slide 5: Refraction and Reflection
Snell’s Law: n1 Sin Φ1 = n2 Sin Φ2
When Φ2 = 90, Φ1 = Φc is the Critical Angle
Φc=Sin-1(n2/n1 )
Notes: 6

## Slide 6: Step Index Multimode Fiber
Fractional refractive-index profile

## Slide 7: Ray description of different fibers

## Slide 8: Single Mode Step Index Fiber
Only one propagation mode is allowed in a given wavelength.
This is achieved by very small core diameter (8-10 µm)
SMF offers highest bit rate, most widely used in telecom

## Slide 9: Step Index Multimode Fiber
Guided light propagation can be explained by ray optics
When the incident angle is smaller than the acceptance angle, the light will propagate via TIR
a Large number of modes possible
Each mode travels at a different velocity
  Modal Dispersion
Used in short links, mostly with LED sources

## Slide 10: Graded Index Multimode Fiber
Core refractive index gradually changes towards the cladding
The light ray gradually bends and the TIR happens at different points
The rays that travel longer distance also travel faster
Offer less modal dispersion compared to Step Index MMF

## Slide 11: Refractive Index Profile of Step and Graded Index Fibers
a
b
n1
n2
n2
n1
a
b
n =
n =
Step
Graded

## Slide 12: Step and Graded Index Fibers

## Slide 13: Total Internal Reflection in Graded Index Fiber

## Slide 14: Total Internal Reflection in Graded Index Fiber - II

## Slide 15: Skew Rays

## Slide 16: Maxwell’s Equations
……..(1) (Faraday’s Law)
E: Electric Field
……….(2) (Maxwell’s Faraday equation)
H: Magnetic Field
……….(3) (Gauss Law)
……….(4) (Gauss Law for magnetism)
Taking the curl of (1) and using and
The parameter ε is permittivity and μ is permeability.
…….(5)
In a linear isotropic dielectric material with no currents and free of charges,

## Slide 17: Maxwell’s Equations
But from the vector identity
……(6)
Using (5) and (3), …….(7)
Similarly taking the curl of (2), it can be shown
………(8)
(7) and (8) are standard wave equations. Note the Laplacian operation is,

## Slide 18: Maxwell’s Equation
Electrical and magnetic vectors in cylindrical coordinates are given by,
.…..(9)
……(10)
Substituting (9) and (10) in Maxwell’s curl equations
….(11)
….(12)
  ….(13)

## Slide 19: Maxwell’s Equation
Also
----------(14)
----------(15)
----------(16)
By eliminating variables, above can be rewritten such that when Ez and Hz are known, the remaining transverse components Er , Eφ, Hr , Hφ, can be determined from (17) to (20).

## Slide 20: Maxwell’s Equation
…………..(17)
…………..(18)
…..........(19)
.………… (20)
Substituting (19) and (20) into (16) results in
….…(21)
…….(22)

## Slide 21: Electric and Magnetic Modes
Note (21) and (22) each contain either Ez or Hz only. This may imply Ez and Hz are uncoupled. However. Coupling between Ez and Hz is required by the boundary conditions.
If boundary conditions do not lead to coupling between field components, mode solution will imply either Ez =0 or Hz =0. This is what happens in metallic waveguides.
  When Ez =0, modes are called transverse electric or TE modes
  When Hz =0, modes are called transverse magnetic or TM modes
However, in optical fiber hybrid modes also will exist (both Ez and Hz are nonzero). These modes are designated as HE or EH modes, depending on either H or E component is larger.

## Slide 22: Wave Equations for Step Index Fibers
Using separation of variables
        ………..(23)
The time and z-dependent factors are given by
        ………..(24)
Circular symmetry requires, each field component must not change when Ø is increased by 2п. Thus
        …………(25)
Where υ is an integer.
Therefore, (21) becomes
        ….(26)

## Slide 23: Wave Equations for Step Index Fibers
Solving (26). For the fiber core region, the solution must remain finite as r0, whereas in cladding, the solution must decay to zero as r∞
Hence, the solutions are
  In the core, (r < a),
  Where, Jv is the Bessel function of first kind of order v
  In the cladding, (r > a),
  Where, Kv is the modified Bessel functions of second kind

## Slide 24
Bessel Functions First Kind
Bessel Functions Second kind
Modified Bessel first kind
Modified Bessel Second kind

## Slide 25: Propagation Constant β
From the definition of modified Bessel function
Since Kv(wr) must go to zero as r∞, w>0. This implies that
A second condition can be deduced from the behavior of Jv(ur). Inside core u is real for F1 to be real, thus,
Hence, the permissible range of β for bound solutions is

## Slide 26: Meaning of u and w
Both u and w describes guided wave variation in radial direction
  u is known as guided wave radial direction phase constant (Jn resembles sine function)
  w is known as guided wave radial direction decay constant (recall Kn resemble exponential function)
Inside the core, we can write,
Outside the core, we can write,

## Slide 27: V-Number (Normalized Frequency)
All but HE11 mode will cut off when b = 0.
Hence, for single mode condition,
Define the V-Number (Normalized Frequency) as,
Define the normalized propagation const b as,

## Slide 30: Field Distribution in the SMF

## Slide 31: Mode-field Diameter (2W0)
In a Single Mode Fiber,
At r = wo,
E(Wo)=Eo/e
Typically Wo > a

## Slide 32: Cladding Power Vs Normalized Frequency
Vc = 2.4
Modes

## Slide 33: Power in the cladding
Lower order modes have higher power in the cladding  larger MFD

## Slide 34: Higher the Wavelength  More the Evanescent Field

## Slide 35: Light Intensity

## Slide 36: Fiber Key Parameters

## Slide 37: Fiber Key Parameters

## Slide 38: Effects of Dispersion and Attenuation
Notes: 7

## Slide 39: Dispersion for Digital Signals

## Slide 40: Modal Dispersion

## Slide 41: Major Dispersions in Fiber
Modal Dispersion: Different modes travel at different velocities, exist only in multimode fibers
This was the major problem in first generation systems
Modal dispersion was alleviated with single mode fiber
  Still the problem was not fully solved

## Slide 42: Dispersion in SMF
Material Dispersion: Since n is a function of wavelength, different wavelengths travel at slightly different velocities. This exists in both multimode and single mode fibers.
Waveguide Dispersion: Signal in the cladding travels with a different velocity than the signal in the core. This phenomenon is significant in single mode conditions.
Group Velocity (Chromatic) Dispersion
= Material Disp. + Waveguide Disp.

## Slide 43: Group Velocity Dispersion

## Slide 44: Modifying Chromatic Dispersion
GVD = Material Disp. + Waveguide dispersion
Material dispersion depends on the material properties and difficult to alter
Waveguide dispersion depends on fiber dimensions and refractive index profile. These can be altered to get:
  1300 nm optimized fiber
  Dispersion Shifted Fiber (DSF)
  Dispersion Flattened Fiber (DFF)

## Slide 45: Material and Waveguide Dispersions

## Slide 47: Different WG Dispersion Profiles
WGD is changed by
adjusting fiber profile

## Slide 48: Dispersion Shifting/Flattening
(Standard)
(Zero Disp. At 1550 nm)
(Low Dispersion throughout)

## Slide 50: Specialty Fibers with Different Index Profiles
1300 nm optimized
Dispersion Shifted

## Slide 51: Specialty Fibers with Different Index Profiles
Dispersion
Flattened
Large area dispersion shifted
Large area dispersion flattened

## Slide 52: Polarization Mode Dispersion
Since optical fiber has a single axis of anisotropy, differently polarized light travels at slightly different velocity
This results in Polarization Mode Dispersion
PMD is usually small, compared to GVD or Modal dispersion
May become significant if all other dispersion mechanisms are small

## Slide 53: X and Y Polarizations
A Linear Polarized wave will always have two orthogonal components.
These can be called x and y polarization components
Each component can be individually handled if polarization sensitive components are used

## Slide 54: Polarization Mode Dispersion (PMD)
Each polarization state has a different velocity  PMD
Notes: 8

## Slide 55: Birefringence
Birefringence is the decomposition of a ray of light into two rays types of (anisotropic) material
In optical fibers, birefringence can be understood by assigning two different refractive indices nx and ny to the material for different polarizations.
In optical fiber, birefringence happens due to the asymmetry in the fiber core and due to external stresses
There are Hi-Bi, Low-Bi and polarization maintaining fibers.

## Slide 56: Total Dispersion
For Multi Mode Fibers:
For Single Mode Fibers:
But Group Velocity Disp.
Hence,
(ΔTpol is usually negligible )
(Note for MMF ΔTGVD ~= ΔTmat

## Slide 57: Permissible Bit Rate
As a rule of thumb the permissible total dispersion can be up to 70% of the bit period. Therefore,

## Slide 58: Disp. & Attenuation Summary

## Slide 59: Fiber Optic Link is a Low Pass Filter for Analog Signals

## Slide 60: Attenuation Vs Frequency
Fiber attenuation does not depend on modulation frequency

## Slide 61: Attenuation in Fiber
Attenuation Coefficient
Silica has lowest attenuation at 1550 nm
Water molecules resonate and give high attenuation around 1400 nm in standard fibers
Attenuation happens because:
  Absorption (extrinsic and intrinsic)
  Scattering losses (Rayleigh, Raman and Brillouin…)
  Bending losses (macro and micro bending)

## Slide 62: All Wave Fiber for DWDM
Lowest attenuation occurs at
1550 nm for Silica
Notes: 1

## Slide 63: Attenuation characteristics
Notes: 3

## Slide 64: Bending Loss
Note:
Higher MFD  Higher Bending Loss

## Slide 65: Micro-bending losses
Notes: 6

## Slide 66: Fiber Production
The Fiber Cable